## Slide 1
Hands-free phone control by hum, pop and hiss.
PROJECT OVERVIEW · VOX / CANTI

## Slide 2
01
Why
CANTI · FLCL
The look: FLCL's robot gives the app its name and colours.
YONDU
The feeling: whistle, and something across the room moves.
THE SPARK
Augmental VOX: a $200 mic you wear to whisper-type. It is just a mic pointed at yourself, so I built my own.
AUGMENTAL
$200
CANTI
~$15–20
And I always wanted an auto-scroller for reels.
Photos: Marvel; Production I.G / Gainax.

## Slide 3
02
What it is
HOW IT WORKS
HEAR
The pendant or the phone mic hears a sound.
DESCRIBE
It becomes one line of text, sent over Bluetooth.
DECIDE
Rules first; a small model for spoken phrases.
ACT
Android swipes, taps or goes back, then checks.
EIGHT SOUNDS
RISE
FALL
ARCH
DIP
FLAT
POP
CLICK
HISS
rise/fall swipe up/down · arch/dip swipe sideways · hiss back · click click home · pop pop listens for a phrase

## Slide 4
03
Who it helps
ACCESSIBILITY
NO TOUCH
Limited hand use, tremor, or busy hands: swipe, tap and scroll by sound.
NO WORDS
Hums, pops and clicks work where speech is hard to recognise; your own sounds count too.
YOUR RANGE
Calibration and training fit each voice. Pitch is relative, never an absolute note.
ONE BUTTON
Arm, stop and pair with presses. Stopping never depends on the mic.
REACH IT ALL
The cursor and "tap the search button" reach what gestures cannot.
Designed for this; not yet tested with disabled users.
LIKE A WIZARD
Whistle, and it moves.
Scroll a recipe with flour on your hands.
Skip a video from across the couch.
Let reels auto-scroll while you do something else.
Next: the desktop and the web.

## Slide 5
04
Demo
UNDER 60 SECONDS
VIDEO
drop the recording here
SHOT LIST
0:00
rise, fall: scroll a list
0:10
arch, dip: swipe sideways
0:18
hiss: back
0:24
click click: home
0:30
pop pop, "open YouTube"
0:40
in Shorts: pop pop, then rise
0:50
pop pop, "tap search"
Phone mic. While a video plays, only "pop pop" gets through.

## Slide 6
05
How it's built
THE PENDANT
BOARD
Pico 2 W
MIC
INMP441
INPUT
one button
CASE
OpenSCAD
TOTAL
~$15–20
Worn as a necklace, lid against the chest. Or skip it: the phone mic works too.
MOVING THE MIC
V1: under the board. Way too hard to work with.
V2: in the lid, on Dupont wires. Unplug the lid and swap the mic.

## Slide 7
06
Models
THE CHAIN
CODE
gestures: instant, exact. No LLM needed.
VERDICT
phrases: 118M, fully on the phone*
CLOUD
the rest: Jev API or Ollama, slower
REAL SCREENS
JEVLIKE
0.465
VERDICT
0.738
CLOUD
0.852
jevlike first → Verdict chosen for phrases → jevlike as teacher → ~12–14 h on the Strix Halo.
PRIVACY
Verdict: nothing leaves the phone.
Ollama, $20/mo: as long as you don't mind giving your info away to China.
*Not shipped yet: "none" recall 0.62, gate 0.8.

## Slide 8
07
Method
MY AGENTIC LOOP
ASK
find the hidden edges; confirm before acting
PLAN
graph out and document everything first
DECIDE
I pick designs and libraries
DISPATCH
Claude plans; Eidolon + DeepSeek execute
VERIFY
tests, parity checks: "looks done" isn't done
ITERATE
measure, loop, hand off
CHALLENGES
MOBILE DEV
New to Android and Dart.
FINE-TUNING
0.447 on real screens at first.
PHONE MIC
Videos made gestures: six layers of guards.
CALIBRATION
A final step per voice; holds up across profiles.

## Slide 9
Try it today***
FOSS, MIT licensed: github.com/dxcently/Canti
*** HUGE asterisks: you still build the APK and turn on the accessibility service. With an Android phone it should just work. Probably. The pendant is optional: the phone mic works.
Questions?

## Slide 10
APPENDIX
The details, for questions.

## Slide 11
10
Tech stack
PENDANT
Pico 2 W: RP2350, BLE
INMP441 I2S mic
OpenSCAD case, PLA
FIRMWARE
C++, arduino-pico 6.1.1
BTstack GATT, LESC
extractor on core 1
PHONE
Kotlin 2.2, no AndroidX
NDK + JNI: same C++
AccessibilityService
on-device speech
UI
Flutter add-to-app
Material 3, no packages
pixel kit + shader
MODELS
PyTorch on ROCm
transformers, ONNX int8
e5: jevlike, Verdict
CLOUD + TOOLS
Jev API, Ollama
DeepSeek executors
Claude agents, Eidolon
NixOS flakes

## Slide 12
11
The sounds
DEFAULT BINDINGS
ONE SOUND
RISE
swipe up
FALL
swipe down
ARCH
swipe right
DIP
swipe left
FLAT
long press
HISS
back
POP
tap
SEQUENCES
HISS CLICK
back
CLICK CLICK
home
CLICK HISS
forward
POP POP
listen
RISE + HOLD
keep scrolling
A lone pop taps only from the pendant; phone-mic pops do nothing. Every binding can be changed per app.

## Slide 13
12
The pendant
HARDWARE
BOARD
Pico 2 W · $7
MIC
INMP441 I2S MEMS
WIRED BUILD
~$15–20
WITH BATTERY
~$25–32
FIRMWARE
vox_node 0.2.2
FLASH / RAM
519 KB / 270 KB
Worn as a necklace in a 3D-printed case. It runs from a USB power bank.
ONE BUTTON
5 PRESSES
arm / off
1 CLICK
gesture ⇄ cursor
HOLD 1 S
disarm, sleep
HOLD 5 S
pair for 60 s
A sound cannot reliably stop the thing that is misreading sounds, so stop lives on the button.

## Slide 14
13
The case
PRINTED PARTS
BASE
LID, INSIDE UP
PLUNGER
presses the button through the lid
MIC CLIP
holds the mic in the lid
PRINT
BASE
back face down · 1
LID
outer face down · 1
PLUNGER
flange down · 1
MIC CLIP
flat · print 2–3, tiny
FIT TEST
optional: board fit
MIC TEST
optional: pocket, 10 min
PLA, 0.2 mm layers, no supports. About 55 × 75 × 20 mm plus the necklace loop.

## Slide 15
14
The mic in the lid
MIC POCKET
C-CLIP
The lid's pocket, printed on its own as mic_test.stl (about 10 minutes) to check the module, foam and clip fit before the whole lid.
THE STACK
fabric disc
lid, 2 mm hole
foam ring
mic, label side up
C-clip
5 wires to the board
THE PLUG
GND
3V3
SD
WS
SCK
A right-angle header, column 9, rows 3–7: the plug lies flat under the lid.
8–9 cm of cable: the lid sets down beside the case, still plugged in.
L/R is bridged to GND on the module, so 5 wires, not 6.

## Slide 16
15
Mapped, then built
BOARD MAP
PICO
MIC ZONE
parts under 4 mm
LED
GP13
BUTTON
GP14
MIC PLUG
col 9, rows 3–7
USB
A 1:1 template (layout.svg): print it, check the 40 mm bar, build the board on it.
BUILD BOOK · 28 STEPS
BREADBOARD · 1–10
1–4 Pico headers, button, LED, flash and test.
5–10 rails, mic wires, L/R bridge, mic level.
NECKLACE · 11–28
11–15 template, place and solder the Pico.
16–21 LED, button, mic header, beep test.
22–28 measure, print, foam ring, plug, mic into the lid, close.
MEASURE FIRST
Measured values drive every hole in the OpenSCAD model. Asserts stop a change that breaks a fit, and the clash check must come out empty.

## Slide 17
16
Listening
EVERY 10 MS
16 KHZ MIC
PITCH
LABEL
Every 10 ms the pendant looks at the last 32 ms of sound, tracks pitch (MPM) and the noise floor, and labels each finished sound: rise, fall, arch, dip, flat, pop, click, hiss or unknown. The code is a C++ port of the Python reference extractor, on the Pico's second core.
HOP COST
16% of budget
CORE 1 LOAD
15.6%
TEST VECTORS
19 / 19 pass
BLE LINK
EVENT
notify
CONFIG
write
INFO
read
Encrypted bonding; new bonds only in a 60 s window.
Every command gets one reply, or times out at 1.5 s.
A dropped link disarms.

## Slide 18
17
On the phone
ANDROID APP
SOURCE
pendant, phone mic or USB mic
GROUP
groups sounds on the device clock
MATCH
matches your enrolled sounds
DECIDE
rules first, a model for hard cases
ACT
gestures via accessibility
GUARDS
Likes, follows and shares need a confirm pop.
A stale screen tree is refused.
Model calls time out; late answers are dropped.
PHRASES
"pop pop" opens a 6 s window.
On-device speech recognition, offline.
Timers, volume, open app, tap a target, type.

## Slide 19
18
Deciding
RULES FIRST
Seconds from the end of a sound to the action (estimates):
FAST PATH
PHONE MODEL
CLOUD MODEL
0
0.25 s
0.5 s
0.75 s
1.0 s
A 225 ms lag tripled pointing errors (MacKenzie & Ware 1993). So fixed bindings act locally, and models only get what rules cannot settle.
WHY CODE WON
FIRST PLAN
A model on the phone picks each next move from your voice training data.
WHAT I FOUND
Once a sound is labelled, a rule is exact and instant. The errors come from hearing, not deciding.
SO
Gestures run on plain code, much quicker and easier. No special LLM needed.

## Slide 20
19
Verdict
ON THE PHONE
You say what to tap; Verdict picks one thing on the screen, or none.
"tap the search button"
Home (button, top left)
Search (button, top right)
Shorts (tab, bottom)
none
MODEL
118M, 2.1 ms on the PC
ON DISK
118 MB, 45 MB pruned
NETWORK
none: 100% local
STATUS
not shipped yet
HOW IT GOT HERE
1
Trained jevlike first: fast, 0.978 on synthetic phrases, but 0.447 on real screens.
2
Verdict did better at picking things by phrase: 0.646 on the same real screens.
3
So Verdict became the model to train and fine-tune.
4
jevlike, fine-tuned earlier, served as its teacher.
5
Fine-tuned on real screens: ~12–14 h total on the Strix Halo (8.75 h of it logged).

## Slide 21
20
Raising the numbers
ACCURACY
Picking the right target on real screens (dev-test, 344 rows):
JEVLIKE
0.465
VERDICT V1D
0.738
CLOUD, FOR SCALE
0.852
Unseen phrasings (synthetic):
BEFORE
0.545
AFTER
0.675
Cloud is smarter but slower (p50 0.7 s) and misses "none" more often (0.43 vs 0.53).
WHAT RAISED THEM
Real screens: 4,648 rows from 613 screens in 57 apps.
A blind second labelling pass: 97% agreement.
Frozen embeddings and a higher learning rate (v1d).
Filler words cut "none" recall to 0.25; a normaliser brings it back to 0.80.
Hidden elements dropped from the options.
Honest scoring: held-out apps, 5-fold cross-fit, a sealed locked test.
wrong taps 0.036, under the 0.05 bound
"none" recall 0.62, gate is 0.8

## Slide 22
21
When it's unsure
THE CHAIN
RULES
gestures: instant and exact
VERDICT
phrases: on the phone, milliseconds
CLOUD
what neither understands: slower, smarter
JEV API
TypeSafe's typed-decision API (Jev).
Put your key in the app's settings; it asks the same /v1/systemone endpoint.
Jev answers in 253 ms median, 437 ms p95 (published desktop figures).
OLLAMA KEY
$20 a month: really cheap DeepSeek, plus whatever other models you can use.
As long as you don't mind giving your information away to China.
Smarter than Verdict on real screens (0.852 vs 0.738), but slower: 0.7 s p50.
Cloud answers are unscored, so risky taps wait for a confirm pop.

## Slide 23
22
Your voice
TRAIN GESTURES
RISE
7/8
FALL
0/8
ARCH
5/8
DIP
0/8
FLAT
0/8
POP
4/4
CLICK
2/4
HISS
0/4
Each take is one variation: hummed or whistled, low or high, slow or quick. Takes save as you go.
ENROL YOUR OWN
CUSTOM SOUND
Invent one (a meow, a trill). It becomes my sound "meow"; bind it with a rule.
IGNORE SOUND
Your sneeze, the kettle. Always does nothing.
YOUR GESTURE
Your own rise or pop, trusted over the default.
3–5 examples each, matched on the phone before any model.

## Slide 24
23
Built with agents
THE LOOP
1
PLAN
Graph out and document everything first: the wiki, a decision log, the risks.
2
DECIDE
I pick the designs and libraries from the options the agents lay out.
3
BUILD
Agents each own one folder and its tests; subagents fan out the grunt work.
4
ITERATE
Try it on the phone, measure, and loop.
THE CREW
LEAD
Claude (Anthropic)
AGENTS
up to ~12 at once
SUBAGENTS
62 for labelling
HARNESS
Eidolon, custom
EXECUTORS
DeepSeek V4.1
OLLAMA PRO
$20 a month
DECISIONS
140+ logged
FIRST BUILD
~24 hours

## Slide 25
24
Challenges
THE PHONE MIC
Videos made gestures: 30–47 would-act sounds a minute, even with Android's echo cancelling. So, layers:
NDK: the pendant's C++ extractor
level gate
media lock, "pop pop" unlocks
no taps from phone-mic pops
lone "up"/"down": pendant only
calibration at the end
The video alone: 0 "pop pop"s in 5.4 min.
ALSO HARD
MOBILE DEV
New to Android and Dart: accessibility, BLE, a launch crash. Now: emulator suite + launch check before any install.
FINE-TUNING
Strong on synthetic data, weak on real screens (0.447) until real screens, blind labels and cross-fit.
DATASETS
4,648 real rows from 613 screens; phone data never leaves the box; a sealed test.
CALIBRATION
A last step that fits the thresholds to each voice. It holds up well across profiles.

## Slide 26
25
Could be cheaper
HARDWARE
Start with no pendant: the phone mic alone works, for $0 of parts.
Print the 10-minute fit tests first: v1 of the case was a whole wasted print.
Skip the LiPo ($8–12): a power bank you already own does the job.
COMPUTE + MODELS
Gestures ended up as plain code, so the gesture-model track could go: jevlike sweeps (8.75 h logged) and Kev 0.8B (dropped).
The teacher labellers scored 0.69–0.79 and never replaced the code labels.
Train only the model you ship. Once Verdict is on the phone, the $20/mo cloud key is optional.

## Slide 27
26
Where it stands
ROUND 6 · 2026-09-27
JVM TESTS
498 / 498 pass
PYTEST
145 pass + 8 xfail
FLUTTER
94 ui + 10 desktop pass
FIRMWARE PARITY
pass
VERDICT WRONG TAPS
0.036 (bound 0.050)
VERDICT NONE RECALL
0.62 (gate 0.8)
EMULATOR SUITE
12 pass · 11 fail
PENDANT MIC
reads all zeros
B4A CROSS-FIT
interrupted, rerun

## Slide 28
27
Next
DO FIRST
1
Find why 11 emulator tests fail: gesture confirmation and cursor taps.
2
Check the pendant mic wiring on the lid header.
3
Rerun the Verdict b4a cross-fit and refit the phone thresholds.
4
Calibrate the phone mic: clicks, whistle, hiss, room.
5
Recapture three screen sets with the badge hidden.
6
Fold this session into the decision log.
HOUSE RULE
Before any phone install: run the emulator suite and a launch check. Unit tests never build the real screen, and that let a launch crash through.